# Text boxes

Max. power			25 W

Max. frequency deviation  	(2.5 kHz for 12.5 Hz  spacing

(5 kHz for 25 kHz spacing

Modulation distortion          max.5%

Spurious radiation	         	max. 0.25(W

FM hum and noise 	         	min. 40 dB for  12.kHz spacing

min. 46 dB for 25 kHz spacing

Receiver

Sensitivity                  	better than 0.25(V (12dBSINAD)

Squelch			adjustable

Audio power			2,5 W ( including loudspeaker )

Audio distortion 		less than 5%

Selectivity                more than 60 dB for 12.kHz spacing

more than  70 dB for 25 kHz spacing

Intermodulation

products attenuation   	more than . 70 dB

Image rejection		more than 70 dB

Frequency range 		146…174 MHz

Number of channels		16

Channel spacing		12.5/25 kHz

Max. channel spread	10 MHz

Working conditions		simplex/ half duplex

Modulation type		MF

Antenna impedance		50 (

Frequency stability		(5 ppm

Power supply		13.6 V (auto battery)

Current consumption

-Transmission	6 A

-Reception		350 mA

-Stand-by		70 mA

Operating temperature range	-10 (C…55 (C

Dimensions			178x145x48 	mm                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                                      (loudspeaker included)

Weight			max. 1500 g

Transmitter

# General specifications

Optional facilities:

·         CTCSS

Consisting of :
-        Transmission-reception unit with mounting support

·         Microphone with fastening clamp

·         Connecting kit (to auto battery)

·          R 8441 A 0 dB antenna (optional)

·         R 8461  3dB antenna (optional)

·         User’s book

MOBILE TRANSCEIVER 
RTM9100 V-M